## Slide 1: IB Physics: Chapter 1
Lesson 5: Uncertainty

## Slide 2: Known Knowns and Known Unknowns.
Watch the video contained in this link.
https://www.youtube.com/watch?v=GiPe1OiKQuk

## Slide 3: Measurements
In Science we are looking for “The Truth”
But to know the truth, we must acknowledge that there are natural limitations to what we can know.
The limitations on our readings exist because.
  Our ability to physically read the instrument to a certain level of precision.
  The ability of the instrument to measure the perfect value.
Speedometer: Pixbay

## Slide 4: Measurements
Look at the reading on the right.
What is your best guess of what the reading is?
My best guess is 43 km/hr, but it could be reading 44 or 42.
  So due to limitations on my ability to read the instrument, I have to acknowledge that there is a range of possibilities, so I would have to say “43±1 km/hr.”
But the instrument itself might have some imprecision based on the calibration. So in reality the uncertainty is considerably larger than we can read.
Speedometer: Pixbay

## Slide 5: Uncertainty
Remember any Scientific measurement contains a certain amount of “uncertainty”
When stating measurements, we want to include a statement quantifying our uncertainty.
Uncertainty is stated using the “±” (plus or minus) symbol.
Eg. Mr Blay is 1.82±0.03 m tall.
  this means that our best guess for his height is 1.82 cm but he might be anywhere between 1.79 m and 1.85 m tall.
You can state uncertainty as
  absolute uncertainty: 1.82 ± 0.03 m
  relative uncertainty using a percentage: 1.82 ± 2% m

## Slide 6: Uncertainty Rules
There are rules that govern how we deal with uncertainty in science.
Rule: Uncertainty must always be 1 Sig Fig.
Rule: The last significant digit in your reading must be the same order of magnitude as your uncertainty.
1.82 ± 0.03 m
is ok
1.82 ± 0.032 m
is not ok
1.82 ± 0.03 m
is ok
1.824 ± 0.03 m
is not ok
1.8 ± 0.03 m
is not ok

## Slide 7: How to make a reading.
Always try to make a reading to the greatest degree of precision as possible.
  You can see that this ammeter is reading before 3 A mark and my best guess is “2.7”
  The absolute limit of any
  instrument is considered
  to be
  “± half the smallest increment”
  here the smallest increment
  is 1A.
  the BEST we can ever state is:
  2.7±0.5 A
  WARNING
  This +/- half the smallest rule
  gives the smallest uncertainty
  you can have. You will usually have a larger uncertainty reading.

## Slide 8: Digital Readouts
Usually a digital instrument will have an uncertainty value published in the manual or on it’s underside… but if you can’t find that, use +/- the last digit.

## Slide 9: Uncertainty from Multiple readings
The best way to get uncertainty from a set of data is to make multiple readings.
  Best guess comes from the “Mean” of the data (the average).
    Add together each reading and divide by number of readings…
  Eg. Time for cart rolling down a a ramp
  (1.10 s+1.06 s+1.15 s+1.11 s+1.17 s)/5
  =1.118 s.
Time 1 (s) | Time 2 (s) | Time 3 (s) | Time 4 (s) | Time 5 (s)
1.10 | 1.06 | 1.15 | 1.11 | 1.17

## Slide 10: Uncertainty from Multiple readings
  Uncertainty is estimated FROM data.
  To get uncertainty from the data: Take half the range in your data.
  Get the largest number: 1.17
  Smallest number: 1.06
  Get the range…. 1.17-1.07=0.11
  Divide the range by 2
  Put it all together and watch out for sig figs.
  1.118 ± 0.055 s (uncertainty has too many sig figs)
  1.118 ± 0.06 s (precision of data and uncertainty don’t agree)
  1.12 ± 0.06 s Correct…
Time 1 (s) | Time 2 (s) | Time 3 (s) | Time 4 (s) | Time 5 (s)
1.10 | 1.06 | 1.15 | 1.11 | 1.17

## Slide 11: Absolute uncertainty/Relative uncertainty/Percentage uncertainty.
If you have a number for example 15±3 cm.
  Then “3” cm is called the “absolute uncertainty”.
  The relative uncertainty is the absolute uncertainty divided by number:
    = 0.2.
  The percentage uncertainty is the relative uncertainty x 100.
    0.2x100 =20% So 15±20%

## Slide 12: Math With Uncertainty
There are rules that govern what we do when doing math with readings with uncertainty.
When Adding or Subtracting two readings with uncertainty…
    Eg: 5.02 ± 0.03 m – 2.80 ± 0.01 m
  ADD the ABSOLUTE uncertainty.
    0.03 + 0.01 = 0.04
  Quote making sure not to mess up your sigfigs.
    =2.22 ± 0.04 m

## Slide 13: Math with uncertainty: Understanding your data booklet.
Your data booklet tells you how to do math with uncertainty, but it is a little confusing. So.
In your data booklet “a”, “b”, and “c”” are readings and “Δa” “Δb” and “Δc” are uncertainties in those readings. So imagine we had a number:
  “15±2” then “15” might be “a” and “2” would be “Δa”.
  “ 8±1” then “8” might be “b” and “1” would be “Δb”.
In your data booklet, y is the answer to any problem and Δy is the uncertainty in that answer.

## Slide 14: Math with uncertainty: Understanding your data booklet.
Your data booklet sais:
If y= a±b
Then Δy= Δa±Δb
This is saying when adding or subtracting two readings (b is either being added to a or subtracting from a)
Then you will add the uncertainties in each.

## Slide 15: Math With Uncertainty: Multiplying and Dividing
When Multiplying or Dividing two readings with uncertainty…
    Eg. 5.02 ± 0.03 m x 2.80 ± 0.01 m
  ADD the RELATIVE UNCERTAINTIES…
    First convert absolute uncertainty to relative…
    and
    Then add these relative uncertainties
    0.0060+0.0036=0.0096
    Then do math!
    5.02x2.80=14.056
    You can convert the relative uncertainty to percent uncertainty by x 100
    14.056 ±0.96%....
    Either round according to sigfig rules
    14.1 ± 1% m2
    Or convert back to absolute uncertainty.
    0.96% of 14.056 = 0.1349376 so…
    14.1 ± 0.1 m2

## Slide 16: Math With Uncertainty: Multiplying and Dividing using the formula sheet.
Your data booklet sais:
If
Then
This is saying multiplying (axb) or dividing (a or b divided by c)
Then you will add relative uncertainties etc… to get the relative uncertainty in the answer .

## Slide 17: Math With Uncertainty
Putting a measurement to a power.
    Eg. (5.02 ± 0.03 m)2
  Multiply the relative uncertainty by the power
    First convert absolute uncertainty to relative…
    Then multiply relative uncertainty by the “power”
      0.0060x2= 0.012 (here “2” is the power)
      And 5.022 = 25.2004
      Then convert ± to percent and rounding to sig figs…
      25.2±1% m2
      Or convert back to absolute uncertainty
      Then quote rounding to sig figs…

## Slide 18: Math With Uncertainty: Multiplying and Dividing using the formula sheet.
Your data booklet sais:
If
Then
This is saying you are raising a to the nth power. (If it was 92 then “a” is 9 and “n” is 2.
Then you will multiply the relative uncertainty of the number by the power to get the relative uncertainty in the answer .

## Slide 19: Math with Uncertainty
Multiplying or Dividing a measurement by a constant.
  Eg… 5.02 ± 0.03 m x 2
  Just multiply the absolute uncertainty by the constant.
    5.02x2 ± 0.03x2 m
    10.04 ± 0.06 m
  Hint… When you do this the RELATIVE UNCERTAINTY REMAINS UNCHANGED.

## Slide 20: References
Speedometer. Pix Bay https://pixabay.com/static/uploads/photo/2011/02/06/21/57/speedo-4781_640.jpg accessed 7/8/2015